## Slide 1
Foodi
Automated modular pet feeding with local AI diet insights
Robotics competition - built on Arduino UNO Q + ESP32-S3 - team: [names]

## Slide 2
The problem
Why pets need Foodi
• Inconsistent portions and irregular feeding times lead to obesity and digestive issues
• Owners are away at work or on trips - feeding still has to happen, on time
• Early appetite changes are the first symptom of many illnesses, and the easiest to miss
• Existing smart feeders dispense food; none of them watch what the pet actually eats
Our answer
• Automated, scheduled, portion-accurate feeding
• Camera + load cell observe every meal
• Local AI learns the eating pattern and flags changes early
• Fully offline: no cloud, no subscription, no privacy leak

## Slide 3
System overview
Two modules, one ecosystem
CCM - Central Computing Module
• Arduino UNO Q (Linux): FastAPI backend, SQLite, scheduler, AI inference
• Wi-Fi + Bluetooth radios, battery management, wall power
Feeder module
• ESP32-S3: auger motor, HX711 load cell, camera
• Own battery + BMS, runs its schedule autonomously
Data flow
• Feeder -> CCM (BLE): weight, food level, meal events
• CCM -> Feeder (BLE): dispense, schedule sync, time sync
• Feeder -> CCM (Wi-Fi): camera stream
• CCM -> owner (Wi-Fi, web app): dashboard, live view, insights
Pairing: owner joins the CCM to the home Wi-Fi, pairs the feeder over
Bluetooth, and the feeder joins Wi-Fi for smooth video.

## Slide 4
Feeder firmware
ESP32-S3, implements the Foodi BLE protocol v1
• Closed-loop dispensing: auger runs fast, then slows near the target; load cell decides when to stop
• Jam / empty-hopper guard: 20 s timeout, motor off on any fault
• Idempotent commands: a retried command id can never dispense twice
• Schedule stored in flash: the feeder feeds on time even with Bluetooth down
• Missed meals are reported to the CCM on reconnect
Status
• Full firmware builds clean in PlatformIO: 23% flash, 10% RAM
• Protocol shared byte-for-byte with the CCM (unit-tested both sides)
• Hard 200 g portion limit enforced on the feeder itself
• Next: flash hardware and run the 24 h soak test

## Slide 5
Local AI
From video + weight to a healthy diet
• YOLOX-nano detector finds the pet at the bowl (cat/dog, COCO pretrained)
• Eating = pet in the bowl region for >= 5 s AND bowl weight decreasing
• Consumed grams per meal, not just dispensed grams
• Rolling-baseline anomaly detection (z-score) on daily intake
• Insights are observations, never diagnoses
Measured on real footage
• 1,375 frames analyzed, pet found in 99%
• 11 ms average inference (max 28 ms) - real-time even on the UNO Q
• Demo insight: intake 45% below the 14-day average for 2 days -> alert

## Slide 6
Live demo
Dashboard on the owner's phone
[ screenshot: dashboard ]
drop dashboard.png into docs/screenshots/ and re-run
[ screenshot: live view with AI overlay ]
drop video.png into docs/screenshots/ and re-run
[ screenshot: daily consumption chart ]
drop chart.png into docs/screenshots/ and re-run
Feed now - schedule - live telemetry over WebSocket - anomaly insight - pre-recorded AI video fallback

## Slide 7
Safety & reliability
A feeding robot must never harm the pet
• Portion clamped twice: CCM limit AND an independent 200 g hard limit in firmware
• Daily maximum enforced by the backend
• Motor is off at boot and after any fault
• Jam / empty hopper -> safe stop + alert
• Idempotent command ids: no double feeding, ever
• Feeder is autonomous: feeds on schedule without Bluetooth or Wi-Fi
• Reconnect with backoff; time + schedule re-sync on every reconnect
• Low-food alert before the hopper runs dry
• 17 automated tests cover protocol, clamps, analytics, and the API

## Slide 8
Roadmap
What the next weeks add
• Flash the firmware on the real ESP32-S3 + HX711 and pass the 24 h soak test
• Live MJPEG camera stream from the feeder to the dashboard (endpoint ready, clip fallback today)
• Per-pet recognition for multi-pet homes (50-100 photos per pet)
• Portion recommendations tuned with a vet, bounded by owner-set limits
• Remote access over HTTPS (Cloudflare Tunnel / Tailscale) with a login
• 48 h unattended run as the final reliability gate

## Slide 9
Foodi - the feeder that watches what your pet actually eats.
Thank you - questions welcome